## Slide 1: A program for building an input file describing ICRP reference voxel phantom for Monte-Carlo calculations
Kiryl Viarenich, Victor Minenko, Kristina Makarevich, Siamion Kutsen, Arkady Khrutchinsky (Institute for Nuclear Problems, BSU)
Notes: I present you a talk on a program for building an input file describing ICRP reference voxel phantoms. International Commission on Radiological protection is an organisation that established main radiation protection quantities.

## Slide 2: INTRODUCTION
Radiation protection is based on calculation of doses (effective dose etc.).
Monte-Carlo simulations are used for calculation of doses.
International Commission on Radiological Protection (ICRP) recommends using voxel phantoms of reference adult male and female (ICRP Publication 110) and a series of pediatric phantoms (ICRP Publication 143) for calculations.
Notes: Our work is in the framework of radiation protection. Dosimetric quantities that refer to protection of human can mostly be calculated not measured. Monte-Carlo method is one of the most feasible methods of calculation of such quantities.

## Slide 3: OBJECTIVE
To create a program that converts initial phantom data into a format suitable for Monte-Carlo calculations.
To calculate organ masses of reference phantoms from available data.
Notes: The objective for this work is to build phantoms for Monte-Carlo calculations from reference phantoms published by ICRP.

## Slide 4: Reference individuals
Reference individual is an idealised human with characteristics defined by the International Commission on Radiological Protection for radiation protection purposes
ICRP Publication 89 : Basic Anatomical and Physiological Data for Use in Radiological Protection: Reference Values (2002) 265 P.
Notes: According to IAEA Safety Glossary, Reference individual is an idealised human with characteristics defined by the International Commission on Radiological Protection for radiation protection purposes. The work on establishment of reference individuals was summarised in ICRP Publication 89 published in 2002. Most anthropometric parameters have low variability. Organ masses and height have variability of about 5-10%. However larger variability appear in people of China and other Asian countries.

## Slide 5: PHANTOMS OF reference individuals
Reference voxel phantoms are created based on Computed tomograms of real people
Voxel phantom consists of a huge number of rectangular parallelepipeds of size ~1×1×5 mm.
Total number of voxels ~ 106..107.
Huge computational resources are required for operating with data and for radiation transport calculations.
Notes: Starting 1992 GSF (Germany) started creation of a complete reference phantoms of adult man and woman, which were eventually adopted by ICRP as reference phantoms.

## Slide 6: AVAILABLE DATA FROM ICRP Publication 110
Array of numbers that describe each point of the phantom (AF.dat, AM.dat etc.)
Table of organ ID, name, tissue number and density (AF_organs.dat, AM_organs.dat etc.)
Table of elemental composition of 53 media (AF_media.dat, AM_media.dat etc.)
List of 53 media with blood ratio (AF_blood.dat)
Composition of bone marrow (AF_spongiosa.dat)
A snippet of Fortran code that reads AF.dat array
Text
files
Notes: AF stands for Adult female, AM – adult male The data describing the phantom is not ready for calculations of doses in organs and tissues.
140 organs and tissues
53 media including air (some are redundant, hence have potential for simplification)
Blood ratio is provided for media, not organs
Data for all phantoms has similar structure, therefore one program can be used.
27 lines of Fortran code

## Slide 7: PROGRAM fantom110
1) selection of phantom (path, voxel size);
2) reading of the array of numbers
2.1) calculation of volumes of organs and tissues
2.2) selection of cropped section of the phantom
3) reading of tables of organs and media
4) writing the output files
Notes: We developed a program for conversion of the source data from ICRP Publications 110 and 143 to MCNP input file.

## Slide 8: WOLFRAM Mathematica CAS
Wolfram Mathematica 12.1 computer algebra system was used for the creation program Fantom110.
The main array of numbers (AF.dat etc.) is read using ReadList function
Notes: in Mathematica

## Slide 9: OPTIONS FOR PHANTOM OUTPUT
Number of slices to write into Monte-Carlo
nslimax – minimal slice
nslimin – maximum slice
Total number of voxels in complete phantom~ 106..107
slice 1
slice 348
nslimin
nlimax
~10 minutes for phantom load in memory
Notes: We were using our phantom for calculation of collimated beams. As the number of voxels in the phantom is rather huge, several Monte-Carlo codes have difficulties in reading this file. To overcome this difficulty, we cropped the phantom. The values of nslimax and nslimin are calculated based on the radiation field+15 cm above and below the volume of primary beam.

## Slide 10: INCLUSION of Hands in the phantom
Whether hands should be included into phantom is decided using “Hands” variable
Arms present
Arms excluded
Notes: For medical radiation procedures patients usually raise hands to give access to exposure of lungs.

## Slide 11: Other INPUT variables
Output files can be split when variable “split” is set to “True”. In this case huge data describing the phantom is written into a separate file. All other input data is written into the main file of small size which is easier to operate.
If variable “RDUM” is set to “True”, then parameters user radiation source are written into input file instead of standard radiation source.
Notes: Usually the calculations are performed for several sources of radiation. I.e.

## Slide 12: FANTOM110 PROGRAM RESULT
Notes: Each number is attributed to an organ or tissue and describes specific point of human body. MCNP input file. The program allows extraction of any additional information from the original data, e.g. the shape or mass of any organ/tissue.

## Slide 13: VERIFICATION OF PHANTOMS
Two different ways of verification were made:
1) comparison of flux to dose conversion coefficients calculated using phantom generated using FANTOM program with reference data from ICRP publication 116.
2) comparison of Specific absorbed Fraction with ICRP Publication 133.
Notes: The resulting phantoms were verified both for internal and external exposure.

## Slide 14: СOMPARIsoN WITH ICRP Publication 116
Fluence to dose conversion coefficients were calculated for unidirectional beams with mono-energetic photons.
Photon energy, keV | Fluence to effective dose CC, AP (current study*), pGy·cm² | Fluence to effective dose CC, AP (ICRP Publication 116) , pGy·cm² | discrepancy (current study-ICRP)/ICRP , %
60 | 0.390 | 0.389 | +0,26
80 | 0.444 | 0.444 | 0
100 | 0.519 | 0.521 | -0,38
* Makarevich KO, Minenko VF, Kuten SA. Dose conversion coefficients for external photon irradiation. Journal of the Belarusian State University. Physics. 2019;1:88 – 96. Russian.
Notes: AP- anterior-posterior, when the unidirectional beam falls on the front of the phantom

## Slide 15: Specific Absorbed fraction
Nuclide | Φ (our study*), kg-1 | ε, % | Φ (based on ICRP Publication 133), kg-1 | discrepancy (our study-ICRP)/ICRP, %
137Cs | 0,692 | 0,15 | 0,685 | 0,6
We calculated Specific absorbed fraction = relative energy deposition per target mass from 137Cs deposited in breast.
* Веренич, К.А. Расчет удельных поглощенных фракций для дозиметрии внутреннего облучения / К.А. Веренич, В.Ф. Миненко, С.А. Кутень // «Современные проблемы радиационной медицины: от науки к практике» (г. Гомель, 29.04.2021 г.) Мат. Междунар. науч.-практ. конф. – Гомель: ГУ «РНПЦ РМиЭЧ», 2021. – С. 26-27.
For monoenergetic photons within source organ S [ORNL/TM-8381/V1]
where m is the number of emitted photons
Es is the initial energy of each photon emitted from S
Di is the contribution of an individual photon history to absorbed dose

## Slide 16: ADVANTAGES and drawbacks
Advantages:
Easy creation of an input file.
Program is free
Disadvantages:
Based on Wolfram Mathematica
Needs update of the input directories.

## Slide 17: Thank you